HERCBIOS.ASM                   PAGE 1                                
THIS SYSTEM IS SHAREWARE, THEREFORE,
IF YOU LIKE THIS PROGRAM, FIND IT USEFUL, AND DECIDE TO USE IT, 
  THEN YOU MUST SEND A $5.00 LICENCE FEE  U.S. TO:
                                      Douglas McDaniels
                                      2627 Arlington Dr #101
                                      Alexandria VA 22306 U.S.A.
   
Hercbios is Copywrite 1988 by Douglas McDaniels.
HOWEVER, HERCBIOS HAS BEEN RELEASED AS SHAREWARE, SO YOU MAY MAKE
ALL THE COPIES THAT YOU WANT, GIVE THEM TO YOUR FRIENDS, AND YOU MAY
PLACE THIS SYSTEM ON BULLETIN BOARDS.(HBIOSARC.EXE is the recomended
format)
   
   First, what is HERCBIOS.COM ?
   All the major video graphics boards for the IBM P.C. series  and
compatibles,  with  the  single  exception  of the Hercules Monochrome
Graphics Adapter, have a built in ROM BIOS (accessed though INT  10H)
that provides the video primitive functions such as the capability to
put a character on the screen. DOS uses these functions to  implement
its  teletype style interface, and these video ROM BIOS functions are
also accessed by many applications programs. There is no  reason  why
video  ROM  BIOS  functions  should  not be provided for the Hercules
Monochrome Graphics Adapter as well, and  that  is  what  HERCBIOS.COM
does. Using HERCBIOS.COM you can now have a 43 line by 90 column text
mode  for  your  M.G.A  (Hercules  compatable)   board,   and   those
application  programs  that  use  only  BIOS  calls for compatibility
should run under this mode.
   
    You may be wondering what mode number I have decided to use for
the  Hercules board. All the IBM video modes have a number associated
with them, for example monochrome text mode is mode  number  7,  while
C.G.A text mode is mode number 3. The decision is quite easy. IBM has
started at 0, and has worked its  way  up  to  mode  20  or  so.  The
negative  numbers  have not been touched by anyone yet, so now is the
time to do so. I have  chosen  mode  -2  (or  254)  as  the  Hercules
monochrome graphics mode, reserving mode -1 for special use. Note that
this leaves room for a whole series of negative mode numbers for  use
by  other  non-IBM  board  manufacturers, and also for negative modes
that provide extensions to the INT 10H functions of already  existing
modes.  This program also implements a mode mapping feature, allowing
the user to redirect program requests for an IBM mode to a request to
change  to one of the negative, non-IBM modes (the special mode -1 is
involved in this feature, see the documentation  for  video  function
00h and the assembly listing for program MODEMAP )
__________________________________________________                   

        HERCBIOS.ASM                   PAGE 2                                


   
   
 Here  are  general user instructions
                                                                and general comments on the use of HERCBIOS.COM:
    To install the program you simply run it, by entering  HERCBIOS
43, HERCBIOS 29, or HERCBIOS followed by some other number at the Dos
prompt.(The meaning of the command line argument is explained  later.
See  also the description of INT 10H function 08h) But to make use of
it you must also load the pixel maps. I have provided an accompanying
mini-program  ASCITABL.COM  which  loads the ASCII pixel bit maps for
IBM computers and true compatibles, and the Dos program  GRAFTABL.COM
loads  the  graphics  pixel  maps  for  those  with Dos 3.x. Just run
HERCBIOS.COM, ASCITABL.COM and GRAFTABL.COM in any order.  For  those
who  are  still  using  Dos  2.x,  I  have  provided a program called
GRAFCHAR.COM which duplicates the function of GRAFTABL.COM. Also, for
machines  which  are not really very IBM compatible, ASCITABL.COM may
not work. I have therefore provided an alternate program ASCICHAR.COM
which should work even on those machines, its disadvantage being that
it takes up more RAM than ASCITABL.COM since it must explicitly  load
the  pixel  maps, while ASCITABL.COM makes use of the pixel maps that
are supposed to be already present in the ROM BIOS.    A  word  about
mini-program  ASCITABL.COM,  this  program simply points INT 44H (the
interrupt reserved by IBM for just this purpose) to point to the  8x8
ASCII  pixel  maps,  which  on  IBM  and  true compatibles are always
located at  0F000:0FA6E,  and  I  have  hard  coded  this  vector  in
ASCITABL.COM.
   
   To  change  into the Hercules mode you could use EGAMODE.COM (as
provided by the ZIFF DAVIS Publishing company) but you will  probably
want  to  use the mini-program CHANGE.COM (included) for this purpose
since it allows the user to decide whether  or  not  to  map  in  the
second  graphics  page,  leaving  it  out in order to provide for the
presence of a CGA card. In order  to  change  to  Hercules  monochrome
graphics  mode,  run  the  mini-program CHANGE.COM . If you provide a
command line argument of 0 (.i.e. type CHANGE.COM 0 ) then the second
graphics  page  (page 1) will be suppressed to allow a CGA compatible
card to reside in your system at  the  same  time  as  your  Hercules
compatible  card. To return to text only mode, in order, for example,
to run  programs  that  write  directly  to  the  screen  simply  run
TEXT.COM,  which  will  return  your  system  to  video  mode  7 (IBM
monochrome text only mode)
   
               
   









__________________________________________________                   

        HERCBIOS.ASM                   PAGE 3                                


   In order to select, at  the  Dos  prompt,  the  number  of  rows
displayed   on   the   screen,  I  have  provided  the  mini-programs
ROWS43.COM, ROWS29.COM, and ROWS25.COM.  Those  users  with  ANSI.SYS
installed  should  run  ROWS25.COM right off, since ANSI.SYS requires
that there be only 25 rows on the screen. For those who chose not  to
use  ANSI.SYS  (and  its  utility is very limited) running ROWS43.COM
will put 43 rows on the screen when in  Hercules  monochrome  graphics
mode,  and  running ROWS29.COM will return the display to the default
value of 29 rows on the screen. (Note that you will probably want  to
clear  the screen right after running these programs since previously
written rows are not altered)

   A caution about CLS: The CLS  command  provided  with  Dos  will
suppress  the  alternate  graphics  page,  since when ANSI.SYS is not
installed, CLS clears the screen by issuing a change mode command  to
the  currently  active  video  mode.  Therefore,  I have provided two
clearscreen mini-programs  CLS0.COM  and  CLS1.COM  which  clear  the
screen, the latter permitting the existence of the alternate graphics
page, the former suppressing it.


   Returning to the command line argument of HERCBIOS,  we  see  in
the  description of function 08H that it reserves enough RAM to store
the character codes for the read character function for the number of
rows  specified  in  the  argument.  No  space  is  reserved to store
character attributes (however, an algorithm is used  that  determines
if  the attribute is inverse video by examining the pixel patterns on
the screen. This algorithm works for all but a very few of  the  more
esoteric characters).
   
   Note  that  line  drawing functions are included with these BIOS
functions.  I  have  included  the  Turbo  C  program  DAZZLE   which
demonstrates  the  efficiency  of  the line drawing routines. Try it!
(But be sure to use CHANGE to change into the new  bios  mode  before
running DAZZLE)

               All names of products used here are trademarks or registered
               trademarks of their respective owners.
   
   This  brings  us  to the actual INT 10H AH functions themselves.
Here follows a writeup of all the supported functions, along with the
features specific to this implementation.
   
   








__________________________________________________                   

        HERCBIOS.ASM                   PAGE 4                                


 SET VIDEO MODE (Function 00H)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:²²²BH²²²°°°BL°°° AH = 00H
CX:²²²CH²²²²²²CL²²² AL = Video mode to select
DX:°°°DH°°°°°°DL°°° BH = Number of highest graphics page to be mapped
                   into memory.(Currently for AL = 254 only)
°°°°°°°SP°°°°°°° CH = IBM mode number to map (AL =  255 only)
°°°°°°°BP°°°°°°° CL = Translation for future requests for mode in CH
°°°°°°°SI°°°°°°°      (AL = 255 only)
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°
   
   
   Exceptions and Comments:
   
   When  AL  =  255  a special mode mapping feature is invoked. Any
future requests for the mode contained in CH will be translated  into
a request for the mode number contained in CL. Also, the current mode
will be changed to mode 7 (monochrome text only)  as  a  side  effect.
Furthermore,    if   mode   254   is   placed   in   CL,   then   the
Get_Current_Display_Mode function  request  when  in  mode  254  will
return  the mode number in CL from then on, instead of 254. To undo a
mode mapping, simply use this function to remap the mode  to  itself.
It  would  probably  be undesirable to put 255 into CH or CL however,
unless you are quite sure that you know what you are doing.
   ______________________________________________________

 SET CURSOR TYPE (Function 01H)
 
AX:²²²AH²²²°°°AL°°° CALL
BX:°°°BH°°°°°°BL°°° AH = 01H
CX:²²²CH²²²²²²CL²²² CH = Starting line within character cell for cursor
DX:°°°DH°°°°°°DL°°° CL = Ending line within character cell for cursor
                                      
°°°°°°°SP°°°°°°°
°°°°°°°BP°°°°°°°
°°°°°°°SI°°°°°°°
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°




__________________________________________________                   

        HERCBIOS.ASM                   PAGE 5                                


   
   
   Exceptions and Comments:
   
   The default setting for mode 254 is CH = 06 and CL  =  07.  This
will  place  the  cursor at the bottom of the usual ASCII characters,
and two scan lines tall. For mode 254 the bottom of the  cursor  must
fit  within  the character cell, which is 12 scan lines if the number
of rows on the screen in less than 30, otherwise 8  scan  lines.  The
cursor does not blink.
   ____________________________
   
   
   
      SET CURSOR POSITION (Function 02H)
 
AX:²²²AH²²²°°°AL°°° CALL
BX:²²²BH²²²°°°BL°°° AH = 02H
CX:°°°CH°°°°°°CL°°° BH = Page number
DX:²²²DH²²²²²²DL²²² DH = Row
              DL = Column
°°°°°°°SP°°°°°°°
°°°°°°°BP°°°°°°°
°°°°°°°SI°°°°°°°
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°
   
   
   Exceptions and Comments:
   
   There  is a separate cursor associated with both page 0 and page
1. This function sets the cursor for the page contained in BH  (0  or
1).  For  mode  254, DH contains the row and may run from 0 to 42, or
from 0 to 28, depending on how many rows to  display  on  the  screen
have been selected. DL may run from 0 to 89 for mode 254.
_________________________________________________________
   
   
   
   









__________________________________________________                   

        HERCBIOS.ASM                   PAGE 6                                


      READ CURSOR POSITION (Function 03H)
 
AX:²²²AH²²²°°°AL°°° CALL
BX:²²²BH²²²°°°BL°°° AH = 03H
CX:²²²CH²²²²²²CL²²² BH = Page number (see function 02H)
DX:²²²DH²²²²²²DL²²²

°°°°°°°SP°°°°°°° RETURN
°°°°°°°BP°°°°°°° CH = Starting line for cursor
°°°°°°°SI°°°°°°° CL = Ending line for cursor
°°°°°°°DI°°°°°°° DH = Cursor's row
              DL = Cursor's column
°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°°
°°°°°°°ES°°°°°°°
   
______________________________________________
   
   
      SET DISPLAYED PAGE (Function 05H)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:°°°BH°°°°°°BL°°° AH = 05H
CX:°°°CH°°°°°°CL°°° AL = Page number
DX:°°°DH°°°°°°DL°°°

°°°°°°°SP°°°°°°°
°°°°°°°BP°°°°°°°
°°°°°°°SI°°°°°°°
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°
   

   Exceptions and Comments:
   
   For mode 254 there are two displayable pages, page 0 and page 1.
Users of this function should make sure that page 1 has  been  mapped
into memory before trying to make use of it.
____________________________________________
   
   






__________________________________________________                   

        HERCBIOS.ASM                   PAGE 7                                


   
      SCROLL UP (Function 06H)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:²²²BH²²²°°°BL°°° AH = 06H
CX:²²²CH²²²²²²CL²²² BH = Attribute for blanked area
DX:²²²DH²²²²²²DL²²² CH = Top left row of window
              CL = Top left column of window
°°°°°°°SP°°°°°°° DH = Bottom right row of window
°°°°°°°BP°°°°°°° DL = Bottom right column of window
°°°°°°°SI°°°°°°° AL = Lines to scroll
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°
   
   
   Exceptions and Comments:
   
   If  bits  0  to 2 are blank and either bit 4,5, or 6 is set then
the attribute is treated as inverse video, and a solid block is  used
as a fill character. If AL = 0, then the window is blanked.
___________________________________________________________
   

      SCROLL DOWN (Function 07H)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:²²²BH²²²°°°BL°°° AH = 07H
CX:²²²CH²²²²²²CL²²² BH = Attribute for blanked area
DX:²²²DH²²²²²²DL²²² CH = Top left row of window
              CL = Top left column of window
°°°°°°°SP°°°°°°° DH = Bottom right row of window
°°°°°°°BP°°°°°°° DL = Bottom right column of window
°°°°°°°SI°°°°°°° AL = Lines to scroll
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°
   
   








__________________________________________________                   

        HERCBIOS.ASM                   PAGE 8                                


   Exceptions and Comments:
   
   If  bits  0  to 2 are blank and either bit 4,5, or 6 is set then
the attribute is treated as inverse video, and a solid block is  used
as a fill character. If AL = 0, then the window is blanked.
___________________________________________________________
        
      READ CHARACTER AND ATTRIBUTE AT CURSOR (Function 08H)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:²²²BH²²²°°°BL°°° AH = 08H
CX:°°°CH°°°°°°CL°°° BH = Page (must be zero in any graphics mode,
DX:°°°DH°°°°°°DL°°° including mode 254)
   
°°°°°°°SP°°°°°°° RETURN
°°°°°°°BP°°°°°°° AH = Attribute (See note below) [***updated**]
°°°°°°°SI°°°°°°° AL = ASCII character code
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°°
°°°°°°°ES°°°°°°°
   
   
   Exceptions and Comments
   
   When  installing  HERCBIOS, you may follow the program name with
an optional command line argument consisting of a number  from  0  to
43.  This  number  reserves  enough  RAM to store the ASCII character
codes for the number of rows that you specified starting from the top
down.  If  a  program  issues a get_char (function 08H) request for a
character in a row higher than you  specified  in  the  command  line
argument,  then  the  ASCII  value  for a space character is returned
instead. This function is used only by programs that  read  from  the
screen. It is usually apparent to the user that he is using a program
that does this, so if the user knows that he will not  be  using  any
programs  that  read  from  the screen in mode 254, then the user can
invoke HERCBIOS without any command line  argument,  which  will  not
reserve  any  space  for  the get_character buffer. This can save the
user up to 43*90 = 3870 bytes, which is almost 4Kb.  Also,  for  mode
254, xor'ed characters do not currently update the get_char buffer.
   The  correct  normal/inverse  attribute will be returned through
the use of an algorithm that determins whether or not a character  is
normal  or  inverse  video  directly  from  the  screen  pixels.  The
algorithm returns the correct attribute for  all  except  characters,
177,178,219,220,  and  222,  and  in  43  row mode a few of the funny
characters in the range 0 to 31 are  also  misread.  This  should  be
sufficient for all but the most unusual screen reading requirements.


__________________________________________________                   

        HERCBIOS.ASM                   PAGE 9                                



   
   
      WRITE CHARACTER (USING ATTRIBUTE) AT CURSOR (Function 09H)
   Note:  For  mode  254,  this  is  the  same function provided by
Function 0AH.
 
AX:²²²AH²²²²²²AL²²² CALL
BX:²²²BH²²²²²²BL²²² AH = 09H/(also AH = 0AH)
CX:²²²CH²²²²²²CL²²² AL = Character to write
DX:°°°DH°°°°°°DL°°° BH = Page
              BL = Attribute
°°°°°°°SP°°°°°°° CX = Replication factor
°°°°°°°BP°°°°°°°
°°°°°°°SI°°°°°°°
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°
   
   Exceptions and Comments
   
   For mode 254, if bit 7 of BL  is  set,  the  character  will  be
xor'ed  into  the  display. If bits 0 to 2 of BL are blank and either
bit 4,5, or 6 of BL is set then the attribute is treated  as  inverse
video.  If  bit  3  of  BL  is  set,  and  bit 7 is not set, then the
character is Or'ed into the display. Xor'ed characters do not  update
the  get_char  buffer. Also, if more characters are written with a CX
greater than 1 than will fit on what remains of the  current  column,
then the result is unpredictable.
______________
   
      WRITE PIXEL (Function 0CH)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:°°°BH°°°°°°BL°°° AH = 0CH
CX:²²²CH²²²²²²CL²²² CX = Column (for mode 254: 0 to 719)
DX:²²²DH²²²²²²DL²²² DX = Row (for mode 254: 0 to 347)
              AL = Pixel color (see below)
°°°°°°°SP°°°°°°°
°°°°°°°BP°°°°°°° RETURN
°°°°°°°SI°°°°°°° None
°°°°°°°DI°°°°°°°
   
°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°°
°°°°°°°ES°°°°°°°
   




__________________________________________________                   

        HERCBIOS.ASM                   PAGE 10                               


   Exceptions and Comments
   
   If bit 7 of AL is set, the pixel will be xor'ed into the screen.
For mode 254, the allowable colors are 0 and 1 for  black  and  green
(or  amber,  white ect.) If higher colors are used, additional pixels
will be placed on the  screen  near  the  selected  dot,  but  in  an
unspecified fashion. The currently displayed video page is used.
____________________________________________________
   
   
           READ PIXEL ON SCREEN (Function 0DH)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:°°°BH°°°°°°BL°°° AH = 0CH
CX:²²²CH²²²²²²CL²²² CX = Column (for mode 254: 0 to 719)
DX:²²²DH²²²²²²DL²²² DX = Row (for mode 254: 0 to 347)
   
°°°°°°°SP°°°°°°°
°°°°°°°BP°°°°°°° RETURN
°°°°°°°SI°°°°°°° AL = Pixel color (0 or 1 for mode 254)
°°°°°°°DI°°°°°°°
   
°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°°
°°°°°°°ES°°°°°°°
   
   
   
           WRITE CHARACTER IN TTY MODE (Function 0EH)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:²²²BH²²²²²²BL²²² AH = 0EH
CX:°°°CH°°°°°°CL°°° AL = Character to write
DX:°°°DH°°°°°°DL°°° BH = Page
              BL = Attribute
°°°°°°°SP°°°°°°°
°°°°°°°BP°°°°°°°
°°°°°°°SI°°°°°°°
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° None
°°°°°°°ES°°°°°°°
   






__________________________________________________                   

        HERCBIOS.ASM                   PAGE 11                               


   Exceptions and Comments
   
   For  mode  254,  if  bit  7  of BL is set, the character will be
xor'ed into the display. If bits 0 to 2 of BL are  blank  and  either
bit  4,5,  or 6 of BL is set then the attribute is treated as inverse
video. Xor'ed characters do not update  the  get_char  buffer.  Bell,
backspace,  linefeed  and  carriage return characters are acted upon,
and the cursor is advanced appropriately. Linewrap is  also  provided
(90 characters per column)
_________________________________________
   
           GET MODE (Function 0FH)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:²²²BH²²²°°°BL°°° AH = 0FH
CX:°°°CH°°°°°°CL°°°
DX:°°°DH°°°°°°DL°°°
             
°°°°°°°SP°°°°°°°
°°°°°°°BP°°°°°°°
°°°°°°°SI°°°°°°°
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°° RETURN
°°°°°°°SS°°°°°°° AL = Current video mode
°°°°°°°ES°°°°°°° BH = Active video page
   
   
   -----------------------------------------
   
   
           GET ROWS (Function 20H/11H)
 
AX:²²²AH²²²°°°AL°°° CALL
BX:°°°BH°°°°°°BL°°° AH = 11H or 20H
CX:²²²CH²²²²²²CL²²²
DX:°°°DH°°°²²²DL²²²
             
°°°°°°°SP°°°°°°° RETURN
°°°°°°°BP°°°°°°° DL = Number of rows seen on screen
°°°°°°°SI°°°°°°° CX = Number of scan lines per character
°°°°°°°DI°°°°°°°       (Unique to non IBM video modes)

°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°°
°°°°°°°ES°°°°°°°




__________________________________________________                   

        HERCBIOS.ASM                   PAGE 12                               


   
   -----------------------------------------
   
           GET SIZE (Function 21H/19H)
 
AX:²²²AH²²²°°°AL°°° CALL
BX:°°°BH°°°°°°BL°°° AH = 19H or 21H
CX:²²²CH²²²²²²CL²²²
DX:²²²DH²²²²²²DL²²²
             
°°°°°°°SP°°°°°°° RETURN
°°°°°°°BP°°°°°°° DX = Number of pixel rows on screen
°°°°°°°SI°°°°°°° CX = Number of pixel columns on screen
°°°°°°°DI°°°°°°°      (unique to non IBM video modes)

°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°°
°°°°°°°ES°°°°°°°
   
   -----------------------------------------------------
   
              SET NUMBER OF ROWS ON SCREEN (Function 22H/1AH)

    
AX:²²²AH²²²²²²AL²²² CALL
BX:°°°BH°°°°°°BL°°° AH = 1AH or 22H
CX:°°°CH°°°°°°CL°°° AL = Number of rows to set on screen (Unique to non
DX:°°°DH°°°°°°DL°°°      IBM video modes)
             
°°°°°°°SP°°°°°°° RETURN
°°°°°°°BP°°°°°°° None
°°°°°°°SI°°°°°°°
°°°°°°°DI°°°°°°°

°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°°
°°°°°°°ES°°°°°°°
   
   ----------------------------------------------
   
          MOVE TO POINT, PREPARE TO DRAW LINE (Function 23H)
   (Unique to non IBM video modes)
 
AX:²²²AH²²²²²²AL²²² CALL
BX:°°°BH°°°°°°BL°°° AH = 23H
CX:²²²CH²²²²²²CL²²² AL = Color and style of line to be drawn, 0 = black
DX:²²²DH²²²²²²DL²²²     1 = green/white/amber ,129 = XOR line into screen




__________________________________________________                   

        HERCBIOS.ASM                   PAGE 13                               


             
°°°°°°°SP°°°°°°° CX = X coordinate of start of line (0 to 719 for
°°°°°°°BP°°°°°°° Hercules and compatibles)
°°°°°°°SI°°°°°°° DX = Y coordinate of start of line (0 to 347 for
°°°°°°°DI°°°°°°° Hercules and compatables)

°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°° RETURN
°°°°°°°ES°°°°°°° None
   

-------------------------------------------------------
   
        
          DRAW LINE (Function 23H)
   (Unique to non IBM video modes)
 
AX:²²²AH²²²°°°AL°°° CALL
BX:°°°BH°°°°°°BL°°° AH = 24H
CX:²²²CH²²²²²²CL²²²
DX:²²²DH²²²²²²DL²²²
             
°°°°°°°SP°°°°°°° CX = X coordinate of end of line (0 to 719 for
°°°°°°°BP°°°°°°° Hercules and compatibles)
°°°°°°°SI°°°°°°° DX = Y coordinate of end of line (0 to 347 for
°°°°°°°DI°°°°°°° Hercules and compatables)

°°°°°°°DS°°°°°°°
°°°°°°°SS°°°°°°° RETURN
°°°°°°°ES°°°°°°° None
   

      Exceptions and Comments
   
   The  start of the line is either set by a move command (function
23H), or else defaults to the  end  of  the  last  line  drawn,  thus
successive  draw  commands  can be used to draw polygons with no need
for any move commands for all but the first point of the  polygon  to
be  drawn. The style of the line (white, black, or XOR) is set by the
last issued move command until changed by another move command.
   
   









__________________________________________________                   

        HERCBIOS.ASM                   PAGE 14                               


   
   -------------------------------------------
   
   
 
   
                          Sincerely,
   
   
   
   
                          Douglas McDaniels
   
   






































__________________________________________________