Conner Peripherals, Inc.
CP3000 Intelligent Disk Drive
Product Manual

Revision II
October, 1990

3081 Zanker Road
San Jose, CA   95134-2128
(408) 456-4500

Notice

Conner Peripherals makes no warranty of any kind 
with regard to this material, including, but not 
limited to, the implied warranties of merchantability 
and fitness for a particular purpose. 

Conner Peripherals shall not be liable for errors contained 
herein or for incidental consequential damages in connection 
with the furnishing, performance, or use of this material.

Conner Peripherals, Inc. reserves the right to change, 
without notification, the specifications contained in this manual.

Copyright Conner Peripherals, Inc. No part of this publication 
may be reproduced or translated into any language in any form 
without the written permission of Conner Peripherals, Inc.

IBM, PC/AT and PC/XT are registered trademarks of 
International Business Machines Corporation.


         Table of Contents

1.0      Scope of Manual   

2.0      Key Features      
 
3.0      Specification Summary
         
3.1      Capacity 
3.2      Physical Configuration     
3.3      Performance       
3.4      Read/Write        
3.5      Power Requirements (Typical)        
3.6      Physical Characteristics   

4.0      Environmental Characteristics

         4.1      Temperature       
         4.2      Humidity 
         4.3      Altitude (relative to sea level)    
         4.4      Reliability and Maintenance         
         4.5      Shock and Vibration        
         4.6      Magnetic Field    
         4.7      Acoustic Noise    
         4.8      Safety Standards  

5.0      Functional Description

         5.1      Read/Write and Control Electronics  
         5.2      Drive Mechanism   
         5.3      Air Filtration System      
         5.4      Head Positioning Mechanism 
         5.5      Reas/Write Heads and Disks
         5.6      Error Correction  
         5.7      Customer Options  

6.0      Electrical Description

         6.1      Power Connectors  
         6.2      Power Connector Pin Description     
         6.3      Task File Interface Connector       
         6.4      Diagnostic Routines        

7.0      Recommended Mounting Configuration

         7.1      Shock Tolerance Features   
         7.2      Mechanically Isolated Mounting Points        

8.0      Electrical Description

         8.1      Signal Levels     
         8.2      Signal Conventions         
         8.3      Pin Descriptions  
                  

1.0      Scope of Manual

This manual describes the key features, specification 
summary, physical characteristics, environmental 
characteristics, functional description, electrical 
interface, recommended mounting configuration, timing 
requirements, Host address decoding, command description, 
operations description, and error reporting for the 
Conner Peripherals model CP3000. 


2.0      Key Features

The CP3000 is a high performance 3.5 inch low-profile (1.00") 
42.8 megabyte (formatted) disk drive with a 28 ms average seek 
time. It is designed to operate on an IBM® PC/AT or equivalent 
in translate mode.  

         Key features of the CP3000 include:

o        Low power requirements enabling battery               
         operation in portable environments
o        High performance rotary voice coil actuator with      
         embedded servo system
o        High shock resistance
o        Internal air filtration system
o        Sealed HDA
o        Automatic actuator latch against inner stop upon      
         power down
o        Microprocessor-controlled diagnostic routines that
         are automatically executed at start-up
o        Automatic error correction and retries
o        Block size:  512 bytes
o        Emulates IBM Task File and supports additional        
         commands
o        Up to two drives may be daisy-chained on this         
         interface
o        Translate mode (17 sectors, 5 heads, 980 cylinders) 
         is supported
o        1:1 interleave
o        Look Ahead Read Capability
o        AC Hysteresis on interface
o        8K Buffer

3.0      Specification Summary

3.1  Capacity

         42.8 Mbytes       Formatted

3.2  Physical Configuration

         Actuator Type                       Rotary Voice-Coil
         Number of Disks                     1
         Data Surfaces                       2
         Data Heads                          2
         Servo                               Embedded
         Tracks per surface                  1045
         Track Density (TPI)                 1400
         Bytes per block                     512
         Sectors per Track          40

The physical parameters of the drive are 1045 cylinders, 
2 heads, and 40 sectors. At power-up, the drive will 
default to the native mode for this drive, which is 
522 cylinders, 4 heads, and 40 sectors. 
This drive supports a translate mode of 980 cylinders, 
5 heads, and 17 sectors. Drives with microcode level 2.32 
and above will also support a translation emulating the 
CP344 native parameters of 805 cylinders, 4 heads, and 
26 sectors. (refer to Initialize Drive Parameters command).


3.3  Performance

         Seek Times        Trk. to Trk.      11.0ms
                           Average           28.0ms
                           Maximum           50.0ms

         Rotational Speed           3557 RPM
         Data Trans. Rate           1.5 Mbytes/sec
         Start Time                 Typical  5 sec
                                    Max.     10 sec

         Stop Time                  Typical 5 sec
                                    Max      10 sec

         Interleave                 1:1
         Buffer Size                8K

The timing is measured through the interface with the drive
operating at nominal DC input voltages. The timing also        
makes the following assumptions:
         
o BIOS overhead and PC system hardware dependency have
  been subtracted from timing measurements.
o The drive is operated using its native drive parameters.
  The average seek time is determined by averaging the seek
  time for a minimum of 1000 seeks of random length over the
  surface of the disk.
  These numbers assume spin recovery is not invoked. If 
  spin recovery is invoked, the maximum could be 40 seconds. 
  Briefly removing power can lead to spin recovery being            invoked.

3.4  Read/Write

         Interface                  Task File
         Recording Method  2 of 7 RLL code
         Recording Density 30,871 bpi
         Flux Density               20,581 rpi

3.5  Power Requirements (Typical)

                           +12VDC   +5VDC    Power
         R/W Mode 230ma    275ma    4.2 W
         Seek Mode         140ma    180ma    2.8 W
         Idle Mode         120ma    120ma    2.0 W
         Standby Mode      10ma     90ma     0.5 W
         Spin-up Mode      700ma    180ma    N/A      

Read/Write Mode:  Occurs when data is being read from or 
written to the disk.

Seek Mode:  Occurs while the actuator is in motion.

Idle Mode:  Occurs when the drive is not reading, writing 
or seeking. The motor is up to speed and DRIVE READY condition 
exists. Actuator is residing on last accessed track. 

Standby Mode:  Occurs when the motor is stopped, actuator 
parked and all electronics except interface control is in 
sleep state.  STANDBY MODE will occur after a programmable 
time-out since last Host access occurs.  Drive ready and seek 
complete status exist.  The drive will leave STANDBY MODE upon 
receipt of a command which requires disk access or upon receipt 
of a spin up command.

Spin-up Mode: Occurs while the spindle motor is accelerating 
from its state to its operational speed. During the typical 
spin-up cycle, current on the 12 volt line may reach up to 900 mA 
for up to 500 microseconds. The specified current is the averaged 
         value over the spin-up cycle. 

Maximum noise allowed (DC to 1 MHZ, with equivalent resistive load)

3.6  Physical Characteristics

         Dimensions        1.00" x 4.00" x 5.75" 
         Weight            1.1 Pound

4.0      Environmental Characteristics

4.1  Temperature

         Operating                  5 deg. C to 55 deg. C
         Non-operating              -40 deg. C to 60 deg. C
         Thermal Gradient  20 deg. C per hr. (Max)

4.2  Humidity

         Operating                  8% to 80% Noncondensing
         Non-operating              8% to 80 Noncondensing
         Max. Wet Bulb              26 deg. C

4.3  Altitude (relative to sea level)

         Operating                  -200 to 10,000 feet
         Non-operating (max)        40,000 feet                

4.4  Reliability and Maintenance

         MTBF                       100,000 hrs. (POH)
         MTTR                       10 Min. typical
         Maint.                     None

4.5  Shock 

         Non-operating              75 Gs
         Operating                  5 Gs*

         *Without nonrecoverable errors

4.6  Magnetic Field

         The externally induced magnetic flux density may not
         exceed six gauss as measured at the disk.

4.7  Acoustic Noise

         40 dBA at a distance of 1 meter from the drive.

4.8      Safety Standards

         The drive is designed to comply with relevant product 
         safety standards such as:

         o  UL 478, 5th edition, Standard for Safety of Information 
         Processing and Business Equipment, and UL 1950, Standard 
         for Safety of Information Technology Equipment 

o        CSA 22.2 #154, Data Processing Equipment and
         CSA 22.2 #220, Information Processing and Business Equipment.

o        IEC 435 Safety Requirements for Data Processing Equipment,
         IEC 380, Safety of Electrically Energized Office Machines, and
         IEC 950, Safety of Information Technology Equipment Including 
         Electrical Business Equipment.

o        VDE 0805 Equivalent to IEC 435,
         VDE 0805 TIEL 100, Equivalent to IEC 950, and 
         VDE 0806, Equivalent to IEC 380.

5.0      Functional Description

         The CP3000 contains all mechanical and electronic parts 
         necessary to interpret control signals, position the recording 
         heads over the desired track, read and write data, and provide 
         a contaminant free environment for the heads and disks.

5.1  Read/Write and Control Electronics

         One integrated circuit is mounted within the sealed enclosure 
         in close proximity to the read/write heads.  Its function is 
         to provide one of two head selections, read pre-amplification, 
         and write data circuitry.

         The single microprocessor controlled circuit card provides the 
         remaining electronic functions which include:

         o        Read/Write Circuitry
         o        Rotary Actuator Control
         o        Interface Control
         o        Spin Speed Control
         o        Dynamic Braking
         o        Power Management

         At power down or the start of STANDBY MODE, the heads are 
         automatically retracted to the inner diameter of the disk.  
         There they are latched and parked on a landing zone that is 
         inside the data tracks.

5.2  Drive Mechanism

         A brushless DC direct drive motor rotates the spindle at 
         3557 rpm.  The motor/spindle assembly is balanced to provide 
         minimal mechanical runout to the disks and to reduce vibration 
         of the HDA.  A dynamic brake is used to provide a fast stop to 
         the spindle motor when power is removed, or upon initiation of 
         STANDBY MODE.

5.3  Air Filtration System

         The head-disk assembly is a sealed enclosure with an integral 
         0.3 micron filter which maintains a clean environment for the 
         heads and disks.

5.4  Head Positioning Mechanism

         The two read/write heads are supported by a mechanism coupled 
         to the voice coil actuator.

5.5  Read/Write Heads and Disks

         Data is recorded on one 95 mm diameter disk through two 3370 
         type composite ferrite heads.

5.6  Error Correction

         The CP3000 performs internal error correction.  The error 
         correction polynomial is capable of correcting one error burst 
         with a maximum of 8 bits per 512 byte block.  The following 
         polynomial is used:

         Forward:  P(X) = (X32+X28+X26+X19+X17+X10+X6+X2+1)

5.7  Customer Options

         There are four jumper options available for configuration:  
         HSP, C/D, DSP, and ACT.  

         HSP, when jumpered, connects the -HOST SLV/ACT signal on 
         the interface to ground for systems that require the slave 
         drive to provide -SLAVE PRESENT signal in a two-drive system.  

         C/D is the address jumper.  When jumpered, the master 
         (or C drive), is selected. When open, the slave (or D drive), 
         is selected.  

         DSP, when jumpered, indicates to the master drive that a slave 
         is present.  In a two-drive system, this jumper option must be 
         installed in the master, or C drive.  

         The last jumper, ACT, connects the -ACTIVE signal to the 
         -HOST SLV/ACT signal on the interface.  This signal provides 
         the capability to drive an external LED.  An external current 
         limiting resistor is required. 

         As an alternative, an LED may be connected between J4, pins 1 
         and 2.  This would provide both an open collector drive signal 
         and a current limiting resistor connected to +5V respectively.




Note 1:  In a two drive system, it is possible to drive one LED 
         with both drives.  An external current limiting resistor 
         is required.  
Note 2:  If the drive is connected to a Host that requires that 
         the signal  -DRIVE SLAVE PRESENT be supplied from the slave 
         drive, via the interface signal -HOST SLV/ACT, then this 
         jumper must be installed.  If this jumper is installed, 
         the ACT jumper must not be installed because the two jumpers 
         are mutually exclusive.


6.0      Electrical Interface

6.1  Power Connectors

         The CP3000 has a 4-pin DC power connector (J3) mounted on the 
         PCB. The recommended mating connector is AMP part number 1-480424-0 
         utilizing AMP pins (part number 350078-4 or equivalent).  
         DC power may also be supplied to the drive through a 3 pin 
         connector (J5). The recommended mating connector is Molex part 
         number 39-01-0033 utilizing Molex pins (part number 39-00-0031 
         or equivalent).  
         Power is to be supplied at either J3 or J5, but not both.


6.3  Task File Interface Connector

         The CP3000 has a 40-pin Task File Interface connector (J2) 
         mounted on the printed circuit board.  The recommended mating 
         connector is Molex part number 10-91-2401 or equivalent.     
         Two drives may be daisy chained together at this connector. 
         Maximum cable length is two feet.  

6.4  Diagnostic Routines

         The microprocessor performs diagnostics upon application of 
         power. If an error is detected, the CP3000 will not come ready.

7.0 Recommended Mounting Configuration

         The CP3000 drive is designed to be used in applications where 
         the unit may experience shock and vibrations at greater levels 
         than larger and heavier disk drives.

7.1  Shock Tolerance Features

         The design features which allow greater shock tolerance are 
         the use of rugged heads and media, a dedicated landing zone, 
         closed loop servo positioning, and specially designed motor 
         and actuator assemblies.    

7.2  Mechanically Isolated Mounting Points

         Ten base mounting points are provided to the customer.  
         The drive is mounted using 6-32 screws; 1/8" maximum insertion 
         for the sides, and 1/4" maximum insertion for the bottom.  
         The system integrator should allow ventilation to the drive to 
         ensure reliable drive operation over the operating temperature 
         range.  The drive may be mounted in any attitude.

         For additional vibration isolation, an external suspension 
         system may be used.  

8.0      Electrical Description

8.1  Signal Levels

         All signal levels are TTL compatible.  A logic "1" is greater 
         than 2.0 volts.  A logic "0" is from 0.00 volts to .70 volts.  

8.2  Signal Conventions

         The interface between the drive adapter and the drive is called 
         the Host Interface. The set of registers in the I/O space of the 
         Host is known as the Task File.

         All signals on the Host Interface shall have the prefix HOST.  
         All negatively active signals shall be further prefixed with 
         a "-" designation.  All positive active signals shall be prefixed  
         with a "+" designation.  Signals whose source are the Host, are 
         said to be "outbound" and those whose source is the drive, are 
         said to be "inbound".

8.3  Pin Descriptions

         The following table describes all of the pins on the Task File 
         Interface:

Signal Name       Dir      Pin      Description

- HOST RESET      O        01       Reset signal from the Host system which 
                                    is active low during power up and 
                                    inactive thereafter.

GND               O        02       Ground between drive and Host.

+HOST DATA        I/O      03-18    16-bit bi-directional data bus 0-
                                    16 between the Host and the drive. 
                                    The lower 8 bits, HD0 - HD7, are 
                                    used for register and ECC access.  
                                    All 16 bits are used for data 
                                    transfers.  These are tri-state 
                                    lines with 24 mA drive capability.

GND               O        19       Ground between drive and Host.

KEY               N/C      20       An unused pin clipped on the drive 
                                    and plugged on the cable. Used to
                                    guarantee correct orientation of the 
                                    cable.

RESERVED O        21       

GND               O        22       Ground between drive and Host.

- HOST IOW        O        23       Write strobe, the rising edge of 
                                    which clocks data from the Host 
                                    data bus, HD0 through HD15, into 
                                    a register or the data register 
                                    of the drive.

GND               O        24       Ground between drive and Host.

- HOST IOR        O        25       Read strobe which, when low, enables
                                    data from a register or the data 
                                    register of the drive onto the Host 
                                    data bus HD0 through HD15.  The 
                                    rising edge of - HOST IOR latches 
                                    data from the drive at the Host.

GND               O        26       Ground between drive and Host.

RESERVED O        27,29    

+HOST ALE         O        28       Host Address Latch Enable. A signal
                                    used to qualify the address lines.  
                                    This signal is presently not used by 
                                    the drive.

GND               O        30       Ground between drive and Host.

+HOST IRQ14       I        31       Interrupt to the Host system,
                                    enabled only when the drive is selected,
                                    and the Host activates the - IEN bit in
                                    the Digital Output register. When the 
                                    -IEN bit is inactive, or the drive is 
                                    not selected, this output is in a high
                                    impedance state, regardless of the state
                                    of the IRQ bit.  The interrupt is set 
                                    when the IRQ bit is set by the drive 
                                    CPU. IRQ is reset to zero by a Host 
                                    read of the Status register or a write 
                                    to the command register.  This signal 
                                    is a tri-state line with 8 mA drive 
                                    capacity.

- HOST IO16       I        32       Indication to the Host system that 
                                    the 16 bit data register has been 
                                    addressed and that the drive is 
                                    prepared to send or receive a 16 
                                    bit data word. This line is a
                                    tri-state line with 24 mA drive 
                                    capacity.

- HOST PDIAG      I        34       Passed diagnostic. Output by the drive 
                                    if it is strapped in the slave mode 
                                    (C/D not jumpered). Input to the drive 
                                    if it is strapped in the master mode 
                                    (C/D jumpered).  This low true signal
                                    indicates to a master that the slave 
                                    has passed its internal diagnostic 
                                    command. This line is a tri-state line 
                                    with 24 mA drive capability.

+HOST A0,         O        35,      Bit binary coded address used to select
     A1, A2                33,36    the individual registers in the task 
                                    file.

- HOST CS0        O        37       Chip select decoded from the Host address 
                                    bus.  Used to select some of 
                                    the Host accessible registers.

- HOST CS1        O        38       Chip select decoded from the Host
                                    address bus. Used to select three of 
                                    the registers in the Task File.

- HOST SLV/ACT    I        39       Signal from the drive used either to 
                                    drive an active LED whenever the disk 
                                    is being accessed or as an indication 
                                    of a second drive present.  (See the 
                                    Customer Options section for further
                                    information.)  When jumpered as 
                                    -ACTIVE, this signal is active low 
                                    when the drive is busy and has a drive
                                    capability of 20 mA.  When jumpered as 
-SLAVE PRESENT                      signal, it is an indication of the 
                                    presence of a second drive when low.  
                                    In this state, it has a 
                                    drive capability of 10 mA open drain.

GND               O        40       Ground between drive and Host.