CalComp Digitizer and Mouse Drivers - PC Edition, Version 2.0
                                 README.DOC


Contents
        
        I .................... Driver Breakdown of Release 2.0
        II ................... General Release Notes
        III .................. Supporting Two Input Devices in Windows
        IV ................... Button Assignments in AutoCAD
        V .................... Tilt Support in Fractal Painter 3.0
        VI ................... Special PenWindows Information
        VII .................. Special Cadvance Information


I - Driver Breakdown of Release 2.0

     There are three main groups of drivers included in Release 2.0 of the 
     CalComp Digitizer and Mouse Drivers:

         1. DOS mouse drivers 
                - CCMOUSE.COM Version 9.03 and support utilities
         2. AutoCAD drivers
                - DGCALCMP.EXP Version 1.4, for use with AutoCAD R11, R12, 
                  R13 for DOS
                - DGCCWT.DLL Version A.1.83, for use with AutoCAD R12 for 
                  Windows (used in conjunction with the WinTAB driver)
         3. Windows WinTAB compatible driver Version 2.0
                - includes Tablet Manager and support files 


II - General Release Notes

 1.  The WinTAB driver will support AutoCAD for Windows R12, R13, and any 
     other Windows application that uses the WinTAB specification. This 
     version also supports the PenWindows Dynamic Link Library (DLL). This 
     means that any application that relies on the PenWindows DLL, such as 
     Microsoft's Pen Extensions for Windows (Windows for Pen Computing) and 
     some pressure sensitive applications, will be supported.

 2.  Version 2.0 of the WinTAB driver now includes CalComp's Tablet Manager 
     for Windows. The Tablet Manager icon and this README.DOC will install 
     into a CALCOMP DIGITIZER group. The Tablet Manager will also be added
     to the "load=" line in the WIN.INI file in order to start automatically
     when Windows is started. If you are upgrading from a previous version
     of CalComp Windows drivers that included a Tablet Manager, we recommend
     you delete the old Tablet Manager icon from the MAIN Windows group.

 3.  The INSTALL program now provides an Un-install option. This option will
     return your system to the configuration used before the CalComp drivers 
     were installed. Although designed to handle most situations, the Un-
     install routine may not know to de-install certain kinds of mouse 
     drivers. If you have problems with your original mouse device after Un-
     installing, we suggest re-installing the drivers for that device.

 4.  Mouse control in a full-screen DOS window in Windows is now supported.
     The latest CCMOUSE.COM (Version 9.03) is needed for this feature to be
     available. To install or upgrade this driver, run the CalComp install
     program and select "1) DOS DRIVERS" from the software options menu. You
     may experience problems such as the pointer not moving when returning
     to Windows from a full-screen DOS window. If so, use the PIF Editor in 
     the MAIN group to edit the DOSPRMPT.PIF file. Make sure that the 
     BACKGROUND box is checked, if not, ckeck it and save the PIF. This 
     should clear up the problem.

 5.  A Pen Pressure utility has been added to the Tablet Manager. This 
     utility will allow the adjustment of the pen tip click level (the 
     pressure level which generates a Button Click for Windows) and the 
     minimum and maximum pressure range values of the pressure sensitive pen. 
     Use caution when adjusting the tip sensitivity level and the pressure 
     range values. Some pressure sensitive applications assume that the 
     minimum pressure range value and the tip click level are approximately 
     the same. In other words, when drawing with a pressure pen, the 
     application first expects a Button Click, then will draw according to 
     the pressure level received. Adjusting them to differ widely may cause 
     unexpected pressure response in these applications. 

        Example:
                Changing the tip click level to 80, but leaving the pressure
                range values at 0 and 255 will result in nothing being drawn
                for pressure levels 0-79 (until the tip click pressure level
                is reached.)
 
 6.  In addition to the Default button set, the Tablet Manager includes two
     other button sets - for AutoCAD R12 and R13, and for Microstation 5.
     These button sets are optimized for these applications which make their
     own button assignments, and are automatically activated when these 
     applications are started.

 7.  The WinTAB driver will now automatically search all COM ports for the
     digitizer. If the driver fails to locate the tablet, or you wish to 
     specify the port, make the following change in the SYSTEM.INI file:

         [pen driver]
         pencom=0     
         calaft=1

     Change the "0" to the number of the COM port where the digitizer is
     connected. Changing this number back to "0" will re-enable the auto-
     search feature.

 8.  As of this release date, the areas generated in the Area Mapping utility
     of the Tablet Manager are mouse-type areas. When in a mapped area on the 
     tablet, the pointing device will act as a mouse, and not support 
     pressure in these mapped areas.

 9.  When configuring a region in the Area Mapping utility, and assigning the 
     region to map to an application window, keep in mind that an application 
     may contain one or more "child" windows within the main window. As you 
     move the pointer over a window, the window border will highlight to 
     assist in the window selection process. The easiest method may be to
     click the title bar of the application you wish to select. 

 10. Certain DOS applications (such as AutoCAD) may cause CCMOUSE to stop 
     working in some DOS mouse programs. If this occurs, and CCMOUSE is 
     already loaded into memory, simply running CCMOUSE again will cause 
     communication with the tablet to be re-esablished, and mouse movement 
     will be restored.


III - Supporting Two Input Devices

 1. The WinTAB driver supports two pointing devices in Windows - a mouse 
    and a digitizer. It is possible to use your current pointing device as 
    the mouse in Windows and use the CalComp tablet in applications that 
    utilize the tablet. To achieve this configuration, you will need the 
    mouse driver MOUSE.DRV loaded in the SYSTEM.INI file. MOUSE.DRV needs 
    to be specified in the "[BOOT]" section on the "MOUSE.DRV=" line. 

        Example:
                [Boot]
                mouse.drv=mouse.drv

 2.  If our installation program does not detect MOUSE.DRV as the mouse 
     driver in Windows, the current mouse driver will be replaced with 
     YESMOUSE.DRV, leaving the tablet as the only pointing device in Windows. 
    
 3.  If the CalComp tablet is the only pointing device in Windows and you 
     wish to add support for an additional mouse, change the "MOUSE.DRV=" 
     line in your SYSTEM.INI file to:

      [Boot]   
      mouse.drv=xxxxx.drv   (xxxxx represents the name of your mouse driver)
 
 4.  LMOUSE.DRV and other mouse drivers will work but may cause problems 
     when their mouse control panels are loaded. Many of the mice on the 
     market today will work with MOUSE.DRV. 
           

IV - Button Assignments in AutoCAD

 1.  In AutoCAD R12 and R13 for DOS and Windows, the AutoCAD button assign-
     ments (i.e. SNAP ON/OFF, ORTHO ON/OFF) are defined by AutoCAD. If you 
     wish to change them, please refer to your AutoCAD documentation for 
     assistance.

 2.  In AutoCAD R12 for Windows, all of the AutoCAD button assignments are
     now available on the cursor when in the MOLE area. Configure AutoCAD to
     use the WinTAB driver, using the following steps as a guide:

        1. Run the Install program located on the Digitizer and Mouse 
           drivers Version 2.0 diskette and choose "2) AutoCAD drivers".
           The file will be copied into the AutoCAD for Windows directory.
        2. Start Windows.
        3. Start AutoCAD R12 for Windows and enter configuration (CONFIG).
        4. Choose "Configure Digitizer" and answer "Y" to choose another
           driver.
        5. Choose the driver "WinTAB Compatible Digitizer - By CalComp".
        6. Configure normally for a Mole area (refer to manual if necessary).
        7. Exit and Save the Configuration (returns you to the drawing area).

 3.  In AutoCAD R13 for Windows, a Mole area is no longer used and AutoCAD 
     will automatically assign it's button functions to the cursor. This is 
     most effective when the Tablet Manager is active and using the ACAD 
     button set, as explained below.

 4.  The Tablet Manager includes a button set for use with AutoCAD R12 and 
     R13. This button set will activate automatically when AutoCAD is 
     started. When the Tablet Manager is active and using the button set for 
     AutoCAD, all AutoCAD button functions are active on the cursor. If any 
     MOUSE buttons (i.e. left/middle/right) are assigned via the Tablet 
     Manager other than the standard "Button0=Left Button" assignment, those 
     buttons will NOT be assigned by AutoCAD. They will continue to function 
     as the MOUSE buttons assigned in the Tablet Manager. When the Tablet 
     Manager is not active, the buttons that are assigned in the WINTAB.INI 
     file will NOT be assigned by AutoCAD. The AutoCAD assignments are, of 
     course, only applicable when AutoCAD is running. 

                                         
V - Tilt Support in Fractal Painter 3.0

 1.  In order for the tilt feature in the Advanced Controls of Fractal 
     Painter 3.0 to function properly, make sure the line "calaft=1" is 
     in the SYSTEM.INI file in the "[Pen Driver]" section, as shown below.
     This is the default setting.
     
        Example:     
           
                [Pen Driver]
                pencom=0
                calaft=1      


VI - Special PenWindows Information

 1.  In the process of developing a driver that supports both WinTAB and 
     the PenWindows interface, some tradeoffs were necessary. CalComp 
     developed the WinTAB driver to primarily support WinTAB-compatible
     application programs.  For additional functionality, the PenWindows
     interface is supported as well. To maximize ease-of-use in most 
     applications, we have elected to install the PenWindows interface, 
     but leave it disabled.
      
 2.  If your application requires PenWindows (i.e. Adobe Photoshop), make a 
     simple change to the SYSTEM.INI file, using the following steps as a 
     guide:

        1. Change to the Windows directory (normally C:\WINDOWS).
        2. Using a text editor, edit the SYSTEM.INI file.
        3. Remove the ";" from the ";penwindows=penwin.dll" line in the 
           "[Drivers]" section:

           Before:             
             
                [Drivers]
                pen=wintab.dll
                ;penwindows=penwin.dll
                ccwtdd=ccwtdd.drv

           After:     
           
                [Drivers]
                pen=wintab.dll
                penwindows=penwin.dll
                ccwtdd=ccwtdd.drv

        4. Save and exit.
        5. Start Windows.

     This change will load the PenWindows DLL to enable support for 
     applications that require the PenWindows interface.
     
 3.  Some applications, including AutoCAD for Windows, may experience some 
     button delays or an occasional lost button press when PenWindows is 
     loaded.
 
 4.  Microsoft Write will display an out-of-memory error message and fail to 
     run when PenWindows is loaded. Contact Microsoft technical support for
     additional information.
    

VII - Special Cadvance Information

 1.  Cadvance for Windows requires a change in our button assignments in
     order to configure correctly. To prepare for the Cadvance configuration, 
     modify the WINTAB.INI file in the Windows directory, using the following 
     steps as a guide:

        1. Change to the Windows directory (normally C:\WINDOWS).
        2. Using a text editor, edit the WINTAB.INI file.
        3. Make the following changes:

          Before:

            Csr0PenBtns=  1  2  7           ;for any Stylus or Chording Puck
            Csr1PenBtns=  1  2  7           ;for 16 Button Non-Chording Puck

          After:
            
            Csr0PenBtns=  1  0  0           ;for any Stylus or Chording Puck
            Csr1PenBtns=  1  0  0           ;for 16 Button Non-Chording Puck

        4. Save and exit.
        5. Start Windows.

     Before you configure Cadvance, make sure the Tablet Manager is not 
     active. This program is usually started when Windows initializes and 
     overrides the default button assignments in the WINTAB.INI file. In
     order for Cadvance to configure properly, the above changes need to be
     made and the Tablet Manager must not be active. To deactivate the Tablet
     Manager, switch to the Tablet Manager Window and choose "Settings" and
     "Exit". After the Cadvance configuration is complete, the changes in the 
     WINTAB.INI can be undone and the Tablet Manager restarted.