September 1992

                      LANsmart Installation
                              for
                D-Link Ethernet Pocket LAN Adapter
                ==================================

This installation procedure applies to the following D-Link products:

                DE-620,DE-620CT,DE-620TP,DE-620AUI,



Files        Contents
-----------  -------------------------------------------------
DE-620.DRV   Driver program for the above-mentioned adapters
DE-620.EXE   Driver program for the above-mentioned adapters


1. RUN LANsmart v.1.26 and v.1.30
==================================

  Follow the procedure below to use the new LANsmart driver program on this
  diskette with LANsmart v.1.26 and v.1.30.

  1) Replace the LANsmart program LANMA05.DRV with the new driver program.
     Example:

      > COPY A:\LANSMART\DE-620.DRV  C:\LANSMART\LANSMA05.DRV

  2) Now, you can use both the menu mode and the command mode to log onto
     the network.  The LOGON command syntax is as follows:

      > LOGON <username> <SRV|WKS> /NET:5 [other parameters]


2. RUN LANsmart version 2.xx & v3.xx
=====================================

  You may use both the menu and the command mode to logon to the network.
  The LOGON command syntax is as follows:

      > LOGON <username> <SRV|WKS> /NET:DE-620 [other parameters]

  The driver program DE-620.DRV should first be copied to the directory
  that contains LOGON.EXE program. /NET:DE-620 specifies to LANsmart your
  network adapter card.