Installing D-Link network adapters for MS Windows for Workgroups
     ================================================================

D-Link network adapters are supplied with a driver disk which includes the
NDIS driver.  The NDIS driver file naming convention used by D-Link is
<NICtype.DOS>, where NICtype stands for DE-620, DE100, DE200, DE220, and etc.

The D-Link NDIS driver programs for DOS are developed following Microsoft
NDIS specification version 2.0.1.  This document is a detailed step-by-step
installation procedure for using D-Link network adapters with MS Windows
for Workgroups operating system.

Naming Conventions
==================

  1.  Starting at this point, we will refer to Windows for Workgroups as
      WFW for simplicity.  Any appearance of WFW within this text will refer
      to the Microsoft Windows for Workgroups operating system.

Installation Procedures
=======================

  1.  Preinstall WFW using the included Novell NE2000 compatible driver. WFW
      will generate a default PROTOCOL.INI and CONFIG.SYS file using the
      selected NE2000 network driver.

  2.  You must modify the generated PROTOCOL.INI and CONFIG.SYS files using
      any text editor. (i.e. MSDOS EDIT)

      --------- modify PROTOCOL.INI ----------

  3.  The PROTOCOL.INI file will have multiple references to the "ms$ne2clone"
      name.  Change all occurances of this name to "D-Link".  In a standard
      PROTOCOL.INI, there should be a total of 7 replacements.

      There would be 4 replacements in the [network.setup] section.  Please
      take note of the following lines in [network.setup] section,
           netcard=...
           lana0=...
           lana1=...

      There will be a [ms$ne2clone] section.  This should also be changed to
      [D-Link].

      In both [MS$NETBEUI] and [MS$IPX] sections, there will be a BINDINGS=
      command line.  The BINDINGS command must be bound to "D-Link".

  4.  There will also be a reference to "ms2000$" in the [D-Link] section
      which needs to be changed to the D-Link NIC type name. (i.e. DE100$,
      DE200$, DE220$, DE300$, DE320$, DE400$, DE600$, DE620$, DE650$, etc.)

  5.  In the [D-Link] section, the "IOBASE" keyword must be changed to
      "IOADDRESS".

      The succeeding pages include working sample of CONFIG.SYS and PROTOCOL.
      INI files for WFW using D-Link DE-620 network adapter.

      --------- modify CONFIG.SYS ----------

  6.  Your CONFIG.SYS will have the following statement for loading the
      "ms2000.DOS" device driver.

           DEVICE=C:\WINDOWS\MS2000.DOS

      Change this line to load the appropriate D-Link NDIS device driver
      of your network adapter.  Using D-Link DE-620 adapter, the line would
      appear as,

           DEVICE=C:\WINDOWS\DE620.DOS

      Note: You would have to copy the appropriate D-Link NDIS driver to
            your WFW directory. (i.e. C:\WINDOWS)



                   D-Link NDIS PROTOCOL.INI User Guide
                   ===================================

         This guide lists the available PROTOCOL.INI keywords for all
         D-Link NDIS device drivers.  Most of the keywords are optional
         and have default values.  The asterisk symbol (*) indicates the
         list of D-Link adapters where the keyword is applicable.

         IOADDRESS - This keyword specifies the base I/O port address used
                     by the D-Link Network Interface Card. This value must
                     match the base I/O address of printer port on your PC,
                     If the adapter is DE-620 or DE-600. Otherwise, it must
                     match the IRQ setting on the NIC. If this keyword is
                     not present, the default value will be 300h.
                     * all D-Link network adapters

         INTERRUPT - This keyword specifies the interrupt line used by the
                     D-Link NIC. This value must match the IRQ of printer
                     port on PC when NIC is DE-620 or DE-600. Otherwise
                     , this value must match the IRQ jumper setting on the
                     NIC. If this keyword is not present, the default
                     value will be 3.
                     * all D-Link network adapters

         DRIVERNAME- This keyword specifies the NIC driver's name.  The NIC
                     driver name follows the NIC adapter type.  (i.e. DE100,
                     DE200, DE220, etc.)
                     *all D-Link network adapters

         BASEMEMORY- This keyword specifies the mapped memory address used
                     by the D-Link NIC.  This value must match the base
                     memory jumper setting on your NIC.  Base memory will
                     only be in effect if the remote boot ROM jumper is
                     enabled.
                     *DE-100, DE-200

         ADAPTERID - This keyword specifies the adapter ID used by D-Link
                     MCA bus card. This value must match the card ID jumper
                     setting on your MCA adapter.
                     *DE-300, DE-320

         NETADDRESS- This keyword specifies the node address (hex) used by
                     your network interface card.  This option is used only
                     if you want to override the node address burned in your
                     NIC.  In this case, the specified address will be used
                     instead of the NIC's actual node address.
                     *all D-Link network adapters



Working samples of WFW CONFIG.SYS and PROTOCOL.INI
==================================================

CONFIG.SYS (using D-Link DE-620 NIC)
------------------------------------
     :
device=c:\windows\himem.sys
device=c:\windows\protman.dos /i:c:\windows
device=c:\windows\workgrp.sys
device=c:\windows\msipx.sys
device=c:\windows\de620.dos            <ÄÄÄÄÄÄÄ D-Link NDIS driver
     :

AUTOEXEC.BAT
------------
     :
c:\windows\net start
c:\windows\msipx
c:\windows\netx
     :

C:\WINDOWS\PROTOCOL.INI (using D-Link DE-620 NIC)
-------------------------------------------------
[network.setup]
version=0x3100
netcard=D-Link,1,D-Link                <ÄÄÄÄÄÄÄ¿
transport=ms$netbeui,MS$NETBEUI                |  Use D-Link NIC
lana0=D-Link,1,ms$netbeui              <ÄÄÄÄÄÄÄÅÄ for Netbios and
transport=ms$ipx,MS$IPX                        |  IPX
lana1=D-Link,ms$ipx                    <ÄÄÄÄÄÄÄÙ

[protman]
DriverName=PROTMAN$
PRIORITY=MS$NETBEUI

[D-Link]                               <ÄÄÄÄÄÄ¿
DriverName=de620$                             ÃÄ This section for
;INTERRUPT=7                                  ³  D-Link NIC
;IOADDRESS=0x378                       <ÄÄÄÄÄÄÙ

[MS$NETBEUI]
DriverName=netbeui$
SESSIONS=5
NCBS=10
BINDINGS=D-Link                        <ÄÄÄÄÄÄÄ¿
LANABASE=0                                     |
                                               |
[MS$IPX]                                       ÃÄ Bind to [D-Link]
DriverName=IPX$                                |
MediaType=Novell/Ethernet                      |
BINDINGS=D-Link                        <ÄÄÄÄÄÄÄÙ