Using the Configuration Program to configure your LCS-8634L

   This section describes how to use the Configuration/Diagnostic Program
named 'LSCFG.EXE' which is contained within the root directory of the utility
diskette we provide you to configure the hardware settings of your
LCS-8634L.

   The factory setting of your LCS-8634L are as following:

       Board Type	: NE2000 (16 bit)
       Medium Type	: 10Base-T/10Base-2 (AUTO)
			  (All of LCS-8634L series except LCS-8634L REV.D1)
			  10 Base-2
			  (LCS-8634L REV.D1)
       I/O Base Address : 300H
       IRQ Number	: IRQ 3
       Remote Boot ROM	: C8000H (8K)
       Zero Wait State	: Disable

   We recommend that after you install the LCS-8634L to your PC, please
excute LSCFG.EXE, the configuration program. LSCFG.EXE can detect that if
your LCS-8634L conflict with other I/O device or not. If conflict exists,
LSCFG.EXE will reconfigure your LSC-8634L to another available I/O base
address, IRQ number, Boot ROM address ... etc. .

 IMPORTANT:
     DO NOT excute LSCFG.EXE after loading the LAN CARD DRIVER of your
   Network Operating System because LSCFG.EXE will re-initialize LCS-8634L.
   This will causes the LAN CARD DRIVER fails to work and unpredictable
   troubles.





 Excute this program

   To excute the program, just specify the filename following the dos prompt.

       For example:
		     A>lscfg <enter>

   Then some message will be shown on your screen as follows:

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     É Main Menu ÍÍÍÍÍÍÍÍÍ»
     º²Board²Setup²²²²²²²²º
     º Run Diagnostic	  º
     º View System Status ºStatus ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     º Exit		  ºal ID      : 080000001075		  ³
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼Type       : NE2000 (16 bit) 	  ³
		   ³ Medium Type      : 10Base-2 (Thin ethernet)  ³
		   ³ I/O Base Address : 300H			  ³
		   ³ IRQ Number       : IRQ 3			  ³
		   ³ Remote Boot ROM  : C8000H (8K)		  ³
		   ³ Zero Wait State  : Disable 		  ³
		   ³ Model Name       : LCS-8634L REV.D1	  ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ





	 Esc-Exit	      -Select 	      ÄÙ-Make choice


   Two windows are opened on the background, and active window is drown
with highlight color (yellow color on VGA) double line. Now you can use
the function key shown at the bottom of your screen to move cursor and
select the item you desire.

   There are four options in the main menu:
      o Board setup --------- To change the hardware configuration.

      o Run Diagnostic ------ To perform a series of hardware tests.

      o View System Status -- To view the used and unused I/O, IRQ and
			      memory of your PC.

      o Exit ---------------- To terminate this program.





 Board Setup

     From the Main Menu, select the "Board Setup".
     The Main Menu window goes behind the Board Status window, and the
  Board Status window becomes active window.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²Setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System É Board Status ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     ³ Exit	   º²Physical²ID²²²²²²:²080000001075²²²²²²²²²²²²²²º
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄº Board Type       : NE2000 (16 bit) 	  º
		   º Medium Type      : 10Base-2 (Thin ethernet)  º
		   º I/O Base Address : 300H			  º
		   º IRQ Number       : IRQ 3			  º
		   º Remote Boot ROM  : C8000H (8K)		  º
		   º Zero Wait State  : Disable 		  º
		   º Model Name       : LCS-8634L REV.D1	  º
		   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼






	 Esc-Exit	       -Select	      ÄÙ-Make choice


   The available function keys are shown at the bottom of the screen.

   The description of items of Board Status Menu are as follows:

     - Physical ID:
	   The 12 digit number is the Physical ID of your LAN Card.
	 You can modify this number by selecting this item. (We recommend
	 you NOT to change this value if not necessary.)
     - Board Type:
	   The type of LAN card that your LCS-8634L is campatiable with.
	 You can select this item to change the Board Type.
     - Medium Type:
	   The network interface of your LCS-8634L currently using. You can
	 change it by selecting this item.
     - I/O Base Address:
	   The first I/O Address where your LCS-8634L currently occupies.
	 The LCS-8634L will occupiy 16 continous I/O port. You can select
	 this item to change the I/O base.
     - IRQ Number:
	   The IRQ line of the ISA slot which your LCS-8634L currently using.
	 To change IRQ Number, just select this item.
     - Remote Boot ROM:
	   It shows the Base Address and Size of memory where the LCS-8634L
	 locates your Boot ROM. If you have a Remote ROM installed on the
	 "Boot ROM Socket" of the LCS-8634L, the contents of this Boot ROM
	 will be mapped to this memory area.
	   You can change the Base Address and Size by selecting this item.
     - Zero Wait State:
	   This option allows you to force each Read/Write command involved
	 with your LCS-8634L to operate under zero-wait state.
	   We recommand you to perform a diagnostic after you enable this
	 option to ensure the LCS-8634L can work properly under Zero-Wait
	 State on your PC because of the deviation of Signal Timing of
	 different PC chip set.
     - Model Name:
	   It shows the Model Name of your LAN card. The LSCFG.EXE version
	2.10 can distinguish the Model of your LCS-8634L series LAN card by
	reading EEPROM data.
	   This field can not be modified.





  o Physical ID:

     To modify the physical ID of LCS-8634L, select "Physical ID" from the
  Board Status menu, the Phycal ID window will appear on your screen.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	  (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²Setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System É Board Status ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     ³ Exit	   º²Physical²ID²²²²²²:²080000001075²²²²²²²²²²²²²²º
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Board Type       : NE2000 (16 bit) 	  ³
		   ³ MediumÉ Physical ID ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
		   ³ I/O Baº	The Physical ID is the address of the nodeº
		   ³ IRQ Nuº on the network. Each incoming packet will be º
		   ³ Remoteº accepted or be rejected by the node accordingº
		   ³ Zero Wº to this number.				  º
		   ³ Model º	We recommend that DO NOT change this valueº
		   ÀÄÄÄÄÄÄÄº if not necessary. A wrong setting will cause º
			   º troubles on your network.			  º
			   º						  º
			   º   Physical ID : 080Û00001075		  º
			   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


 Esc-Previous   -Move cursor  0..9,A..F-Input HEX number  ÄÙ-Confirm change

     Now, you can input a 12-digit Hex number to replace the orginal ID.

 IMPORTANT:
     A standard IEEE 802.3 packet kas a Destination address field that
  indicates the destination of the packed on the network and is used to
  filter unwanted packets from reaching a node.
     The LCS-8634L compares the destination address field of the incoming
  packet to its Physical ID to determine whether to accept this packet or
  not.
     We recommand you NOT to change this value if not necessary. A wrong
  setting will cause serious troubles on your network.





  o Board Type

     The LCS-8634L is conpatible with three kinds of LAN card that are well-
  known all over the world:
	 1. Novell NE2000
	 2. Novell NE1000
	 3. Western digital WD8013
     To change the board type of your LCS-8634L, select "Board Type" from
  Board Status menu.
     The Board Type window appears.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²Setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System Ú Board Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Exit	   ³ Physical ID      : 080000001075		  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³²Board²Type²²²²²²²:²NE2000²(16²bit)²²²²²²²²²²²³
		   ³ Medium Type      : 10Base-2 (Thin ethernet)  ³
		   ³ I/O Base Address : 300H	   É Board Type ÍÍÍÍÍ»
		   ³ IRQ Number       : IRQ 3	   º²NE2000²(16²bit)²º
		   ³ Remote Boot ROM  : C8000H (8K)º NE1000 ( 8 bit) º
		   ³ Zero Wait State  : Disable    º WD8013 (16 bit) º
		   ³ Model Name       : LCS-8634L RÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ






	 Esc-Exit	       -Select		ÄÙ-Make choice

     Use the function keys shown at the bottom of the screen to select the
  board type you desire.





  o Medium Type

   You have four choices of medium type of LCS-8634L:
      1. 10Base-T/10Base-2 Auto-detect
	     If you select this option, your LCS-8634L can select the medium
	   interface -- BNC port or RJ45 phone jack which is connected to the
	   cable of your network, automatically.
      2. 10 Base-2
	     Set the BNC connector to be the medium interface of the
	   LCS-8634L.
      3. 10 Base-5
	     Set the AUI port to be the medium interface of the LCS-8634L.

     To change the medium type of LCS-8634L, select "Medium Type" from Board
  Status menu.
     The Medium Type window appears.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²Setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System Ú Board Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Exit	   ³ Physical ID      : 080000001075		  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Board Type       : NE2000 (16 bit) 	  ³
		   ³²Medium²Type²²²²²²:²10Base-2²(Thin²ethernet)²²³
		   ³ I/O Base Address : 300H			  ³
		   ³ IRQ Number       : IRQ 3			  ³
		   ³ ReÉ Medium Type ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»		  ³
		   ³ Zeº 10Base-T/10Base-2 (AUTO)  º		  ³
		   ³ Moº²10Base-2²(Thin²ethernet)²²ºV.D1	  ³
		   ÀÄÄÄº 10Base-5 (Thick ethernet) ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
		       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼





	 Esc-Exit	       -Select		ÄÙ-Make choice

     Use the function keys shown at the bottom of the screen to select the
  appropriate medium type.
     To avoid that you may select the media type which the board doesn't
  support, the unavailable option(s) is(are) shown with gray color, and the
  cursor skips them.





  o I/O Base Address

     To change the I/O base address setting of your LCS-8634L, from the Board
  Status menu, select "I/O Base Address".
     The I/O Address window appears.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	    ShineNET LCS-8634L Setup & Diagnostic Program  V1.00	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿			      É I/O Address ÍÍÍ»
      ³²Board²setup²²²²²²²²³			      º   200H -- 21FH º
      ³ Run Diagnostic	   ³			      º   220H -- 23FH º
      ³ View System Ú Board Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº   240H -- 25FH º
      ³ Exit	    ³ Physical ID      : 080000001021 º  260H -- 27FH º
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Board Type       : NE2000 (16 biº   280H -- 29FH º
		    ³ Medium Type      : 10Base-2 (Thiº   2A0H -- 2BFH º
		    ³²I/O²Base²Address²:²300H²²²²²²²²²º   2C0H -- 2DFH º
		    ³ IRQ Number       : IRQ 3	      º  2E0H -- 2FFH º
		    ³ Remote Boot ROM  : C8000H (8K)  º²²²300H²--²31FH²º
		    ³ Zero Wait State  : Disable      º   320H -- 33FH º
		    ³ Model Name       : LCS-8634L REVº   340H -- 35FH º
		    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº   360H -- 37FH º
						      º   380H -- 39FH º
						      º  3A0H -- 3BFH º
						      º  3C0H -- 3DFH º
						      º  3E0H -- 3FFH º
						      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Esc-Exit	      -Select 	       ÄÙ-Make choice

     Use the function keys shown at the bottom of the screen to select the
  appropriate I/O base address.
     To avoid the setting that may conflict with other board, the I/O address
  have been occupied by other devices are marked with a smile face sign and
  shown with gray color, and the cursor skips them.





  o IRQ Number

     To change the IRQ number setting of your LCS-8634L, from the Board Status
  menu, select "IRQ Number".
     The IRQ Number window appears.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	   ShineNET LCS-8634L Setup & Diagnostic Program  V1.00 	    º
º	(C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	    º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System Ú Board Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Exit	   ³ Physical ID      : 080000001021	   ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Board Type       : NE2000 (16 bitÉ IRQ Number ÍÍÍÍÍ»
		   ³ Medium Type      : 10Base-2 (Thinº²²²IRQ²Level²²3²²º
		   ³ I/O Base Address : 300H	      º  IRQ Level  4	º
		   ³²IRQ²Number²²²²²²²:²IRQ²3²²²²²²²²²º   IRQ Level  5	º
		   ³ Remote Boot ROM  : C8000H (8K)   º   IRQ Level  9	º
		   ³ Zero Wait State  : Disable       º   IRQ Level  10 º
		   ³ Model Name       : LCS-8634L REV.º   IRQ Level  11 º
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº   IRQ Level  12 º
						      º   IRQ Level  15 º
						      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼



	Esc-Exit	      -Select 	       ÄÙ-Make choice

     Use the function keys shown at the bottom of the screen to select the
  appropriate IRQ number.
     To avoid the setting that may conflict with other board, the IRQ have
  been occupied by other devices are marked with a smile face sign and shown
  with gray color, and the cursor skips them.





  o Remote Boot ROM

     The LCS-8634L provides four different sizes of Remote Boot ROM:
	 8K, 16K, 32K, 64K

     The range of ROM base address is from C0000H to DE000H. The number of
  ROM base option depend on the size of the Boot ROM. If you choose 8K as
  your Boot ROM size, the number of the base address option will be up to 16.
  If you choose 64K as your Boot ROM size, the number of the base address
  option is 2 only.
     To change the Boot ROM setting of your LCS-8634L, from the Board Status
  menu, select "Remote Boot ROM".
     The ROM Size window will appear first to ask you to set the Boot ROM size.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System Ú Board Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Exit	   ³ Physical ID      : 080000001075		  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Board Type       : NE2000 (16 bit) 	  ³
		   ³ Medium Type      : 10Base-2 (Thin ethernet)  ³
		   ³ I/O Base Address : 300H			  ³
		   ³ IRQ Number       : IRQ 3			  ³
		   ³²Remote²Boot²ROM²²:²C8000H²(8K)²²²²²²²²²²²²²²²³
		   ³ Zero Wait State  : Disable 		  ³
		   ³ ModeÉ ROM Size ÍÍÍÍÍ»S-8634L REV.D1	  ³
		   ÀÄÄÄÄÄº²²8²Kilo-Bytes²ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
			 º 16 Kilo-Bytes º
			 º 32 Kilo-Bytes º
			 º 64 Kilo-Bytes º
			 º NO Boot ROM	 º
			 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Esc-Exit	      -Select 	       ÄÙ-Make choice

     Use the function keys shown at the bottom of the screen to select the
  size of the Boot ROM.





   After this step, the ROM Address window is opened on your screen.
   In this example, the Boot ROM Size is 8K.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿		   É ROM Address ÍÍÍÍÍÍÍ»
     ³²Board²setup²²²²²²²²³		   º  C0000H -- C1FFFH º
     ³ Run Diagnostic	  ³		   º  C2000H -- C3FFFH º
     ³ View System Ú Board Status ÄÄÄÄÄÄÄÄÄº   C4000H -- C5FFFH ºÄ¿
     ³ Exit	   ³ Physical ID      : 080º   C6000H -- C7FFFH º ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Board Type       : NE2º²²²C8000H²--²C9FFFH²º ³
		   ³ Medium Type      : 10Bº   CA000H -- CBFFFH º ³
		   ³ I/O Base Address : 300º   CC000H -- CDFFFH º ³
		   ³ IRQ Number       : IRQº   CE000H -- CFFFFH º ³
		   ³²Remote²Boot²ROM²²:²C80º   D0000H -- D1FFFH º ³
		   ³ Zero Wait State  : Disº   D2000H -- D3FFFH º ³
		   ³ ModeÉ ROM Size ÍÍÍÍÍ»Sº   D4000H -- D5FFFH º ³
		   ÀÄÄÄÄÄº²²8²Kilo-Bytes²ºÄº   D6000H -- D7FFFH ºÄÙ
			 º 16 Kilo-Bytes º º   D8000H -- D9FFFH º
			 º 32 Kilo-Bytes º º   DA000H -- DBFFFH º
			 º 64 Kilo-Bytes º º   DC000H -- DDFFFH º
			 º NO Boot ROM	 º º   DE000H -- DFFFFH º
			 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Esc-Exit	      -Select 	       ÄÙ-Make choice

     Use the function keys shown at the bottom of the screen to select the
  base address of the Boot ROM.
     To avoid the setting that may conflict with other board, the memory blocks
  have been occupied by other devices are marked with a smile face sign and
  shown with gray color, and the cursor can not move on them.





  o Zero wait

     To enable or disable the wait state, just move the cursor on "Zero Wait
  State" and press Enter Key. The status of this option will switch to another,
  either Enable or Disable.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System É Board Status ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     ³ Exit	   º Physical ID      : 080000001075		  º
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄº Board Type       : NE2000 (16 bit) 	  º
		   º Medium Type      : 10Base-2 (Thin ethernet)  º
		   º I/O Base Address : 300H			  º
		   º IRQ Number       : IRQ 3			  º
		   º Remote Boot ROM  : C8000H (8K)		  º
		   º²Zero²Wait²State²²:²Disable²²²²²²²²²²²²²²²²²²²º
		   º Model Name       : LCS-8634L REV.D1	  º
		   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼






	Esc-Exit	      -Select 	       ÄÙ-Make choice





 Save your setting into the EEPROM of the LCS-8634L

     When you finish the configuration of your LCS-8634L, press ESC key to
  exit this menu.
     If you have maked some changes, the LSCFG.EXE will give you some messages
  before you back to Main Menu -- a Warning window appears on your screen, and
  asks you if you want to save the new configuration into the EEPROM of your
  LCS-8634L or not.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³²Board²setup²²²²²²²²³
     ³ Run Diagnostic	  ³
     ³ View System Ú Board Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Exit	   ³ Physical ID      : 080000001075		  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Board Type       : NE2000 (16 bit) 	  ³
		   ³ Medium Type      : 10Base-5 (Thick ethernet) ³
		   ³ I/O BasÉ Save New Configuration ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
		   ³ IRQ Numº	 The Configuration of your LCS-8634L had º
		   ³ Remote º been modified, do you want to save the new º
		   ³ Zero Waº Configuration to the EEPROM ?		 º
		   ³ Model Nº						 º
		   ÀÄÄÄÄÄÄÄÄº	 ²Yes,²save²it²²     Oh! No, no...	 º
			    º						 º
			    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼




      Y-Yes	      N-No	    -Select	     ÄÙ-Make choice

     Use the function keys shown at the bottom of the screen to make your
  choice.





 Run Diagnostic

     From the Main Menu, select "Run Diagnostic".
     The Diagnostic window appears. After seconds of performing self-testing,
  the results of the diagnostic are shown in this window.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿
     ³ Board setup	  ³
     ³²Run²Diagnostic²²²²²³
     ³ View System Status ³Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Exit		  ³al ID      : 080000001075		  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙType       : NE2000 (16 bit) 	  ³
		   ³ Medium Type      : 10Base-2 (Thin ethernet)  ³
		   ³ I/O Base Address : 300H			  ³
		   ³ IRQ NumÉ Diagnostic ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
		   ³ Remote º Internal Register test............. Pass	  º
		   ³ Zero Waº EEPROM test........................ Pass	  º
		   ³ Model Nº Buffer test (I/O mode)............. Pass	  º
		   ÀÄÄÄÄÄÄÄÄº Loop Back Mode 1 test ............. Pass	  º
			    º Loop Back Mode 2 test ............. Pass	  º
			    º Cable connection test ............. Testing º
			    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼





     After this diagnostic, you can press ank key to back to Main Menu.





 View System Status

     From the Main Menu, select "View System Status".
     Several windows appear on your screen and will show out occupied I/O
  addresses, IRQ numbers and Memory blocks respectively.
     The places by other devices are marked with a smile face sign. The place
  where occupied by your LCS-8634L is marked with a asterisk.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	     ShineNET LCS-8634L Setup & Diagnostic Program V2.10	     º
º	 (C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Ú Main Menu ÄÄÄÄÄÄÄÄÄ¿    É I/O Occupied ÍÍ»  É UMB Occupied ÍÍÍÍÍÍ»
     ³ BoaÉ IRQ Occupied ÍÍÍ»  º   200H -- 21FH º  º  C0000H -- C1FFFH º
     ³ Runº * IRQ Level  3  º  º   220H -- 23FH º  º  C2000H -- C3FFFH º
     ³ Vieº  IRQ Level  4  ºatº   240H -- 25FH ºÄÄº   C4000H -- C5FFFH º
     ³ Exiº   IRQ Level  5  º Iº  260H -- 27FH º07º   C6000H -- C7FFFH º
     ÀÄÄÄÄº   IRQ Level  9  ºpeº   280H -- 29FH º6 º * C8000H -- C9FFFH º
	  º   IRQ Level  10 ºypº   2A0H -- 2BFH º(Tº   CA000H -- CBFFFH º
	  º   IRQ Level  11 º Aº   2C0H -- 2DFH º  º   CC000H -- CDFFFH º
	  º   IRQ Level  12 ºerº  2E0H -- 2FFH º  º   CE000H -- CFFFFH º
	  º   IRQ Level  15 ºooº * 300H -- 31FH ºK)º   D0000H -- D1FFFH º
	  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼t º   320H -- 33FH º  º   D2000H -- D3FFFH º
		   ³ Model Nameº   340H -- 35FH º Rº   D4000H -- D5FFFH º
	  É Symbol ÍÍÍÍÍÍÍÍÍ»ÄÄº   360H -- 37FH ºÄÄº   D6000H -- D7FFFH º
	  º   Free	    º  º   380H -- 39FH º  º   D8000H -- D9FFFH º
	  º * LCS-8634L     º  º  3A0H -- 3BFH º  º   DA000H -- DBFFFH º
	  º  Other devices º  º  3C0H -- 3DFH º  º   DC000H -- DDFFFH º
	  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼  º  3E0H -- 3FFH º  º   DE000H -- DFFFFH º
			       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


     You can press ank key to back to Main Menu.





 Message of confilct with other devices

     LSCFG.EXE will give you some warning message if your LCS-8634L conflict
  with other device. These message are described as following:

  o I/O conflict

     If your LCS-8634L use the same I/O address as other devices, LSCFG.EXE
  will give you this message.
     A Conflict I/O window is opened on the screen. The message contained
  within this window explain that there is another device using the same I/O
  address as your LCS-8634L, shows the I/O address and ask you would like to
  let LSCFG.EXE choose an avaliable I/O for you or not.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	   ShineNET LCS-8634L Setup & Diagnostic Program  V1.00 	    º
º	(C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	    º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	   É Conflict I/O ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	   º	 There is another device in your PC system using º
	   º the same I/O address which your LCS-8634L currently º
	   º using (280H - 29FH). This situation would make your º
	   º PC system and LCS-8634L fail to work.		 º
	   º	 In order to keep your system works correctly,	 º
	   º you can do the followings :			 º
	   º							 º
	   º	 Would you like ...				 º
	   º - Let LSCFG.EXE relocate your LCS-8634L to another  º
	   º   available I/O address.				 º
	   º							 º
	   º	 or ... 					 º
	   º - Exit LSCFG.EXE ,power-off your PC system, and	 º
	   º   remove the device which conflict with LCS-8634L.  º
	   º							 º
	   º	  Please use  key & ÄÙ key to make choice.	 º
	   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


     You can use the function keys shown in the window to make your choice.
     The selected option is highlighted. Press Enter key will make the option
  be chosen.





     If you choose the first option -- Let LSCFG.EXE relocate your LCS-8634L
  to another available I/O address, LSCFG.EXE will show another message to
  tell you where the new I/O base addresses of your LSC-8634L is.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º	   ShineNET LCS-8634L Setup & Diagnostic Program  V1.00 	    º
º	(C)Copyright LONGSHINE Electronics Corp., 1992, 1993, 1994	    º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	   Ú Conflict I/O ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	   ³	 There is another device in your PC system using ³
	   ³ the same I/O address which your LCS-8634L currently ³
	   ³ using (300H - 31FH). This situation would make your ³
	   ³ PC system and LCS-8634L fail to work.		 ³
   É New I/O address ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º  The I/O address of your LCS-8634L is relocated to 200H - 21FH.	  º
   º									  º
   º	 If you don't like this setting, you can select 'LCS-8634L Setup' º
   º  from the Main Menu to change the I/O setting.			  º
   º			  Press any key to continue .....		  º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
	   ³	 or ... 					 ³
	   ³ - Exit LSCFG.EXE ,power-off your PC system, and	 ³
	   ³   remove the device which conflict with LCS-8634L.  ³
	   ³							 ³
	   ³	  Please use  key & ÄÙ key to make choice.	 ³
	   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


  o IRQ conflict

     If your LCS-8634L use the same IRQ number as other devices, LSCFG.EXE
  will give you this message.
     A Conflict IRQ window is opened on the screen which just like Conflict
  I/O window.  The message within this window explain that there is another
  device using the same IRQ as your LCS-8634L, shows the IRQ number and ask
  you would like to let LSCFG.EXE choose an avaliable IRQ for you or not.

     If you choose the first option -- Let LSCFG.EXE reconfigure the IRQ
  setting of your LCS-8634L to another available IRQ, LSCFG.EXE will tell
  you the new IRQ of your LSC-8634L.

  o Memory conflict

     If your LCS-8634L use the same ROM address as other devices, LSCFG.EXE
  will give you this message.
     A Conflict Memory window is opened on the screen which just like Conflict
  I/O window and Conflict IRQ window.  The message within this window explain
  that there is another device using the same Memory Area as your LCS-8634L,
  shows the address of the Memory Area and ask you would like to let LSCFG.EXE
  choose an avaliable Memory Area for you or not.

     If you choose the first option -- Let LSCFG.EXE choose another available
  Memory Area for the Boot ROM of your LCS-8634L, LSCFG.EXE will tell you where
  is the new Memory Area of your LSC-8634L.



---- End of file ----